## Slide 1: IC Design HW2 Tutorial
Yi-Hsiang Chen
Advisor: Tzi-Dar Chiueh
Oct. 23 2012

## Slide 2: Outline
Connect to workstations
Flow chart
Cadence tool
Post-layout simulation tool
Debug tool
Reminder

## Slide 3: Connect to Workstations
PuTTY
Xming
SSH (SFTP)

## Slide 4: Preparatory Works
Download and install program of PuTTY
  http://the.earth.li/~sgtatham/putty/latest/x86/putty.exe
  We will use putty to connect to workstation
Download and install program of Xming
  http://ncu.dl.sourceforge.net/project/xming/Xming/6.9.0.31/Xming-6-9-0-31-setup.exe
  http://sourceforge.net/projects/xming/files/Xming-fonts/7.5.0.25/Xming-fonts-7-5-0-25-setup.exe/download
  Launch GUI in Linux Environments
Download and install SFTP software
  SSH2 in Cuteftp
  SSH in FileZilla (Recommended) http://filezilla-project.org/
  Up/download files to/from workstation

## Slide 5: Launching Xming (1/2)
Install and Setup
  Just click on “next” in each step

## Slide 6: Launching Xming (2/2)
Launch Xming before using putty

## Slide 7: Launching PuTTY (1/2)
Workstation list: http://cad.ee.ntu.edu.tw/ws_list.htm

## Slide 8: Launching PuTTY (2/2)
1
2
3
4
5
6
7

## Slide 9: Log-In (1/2)

## Slide 10: Log-In (2/2)
User Name
  Ex: r98943032 -> r98032
  b97901020 -> b97020
  Ex: b96502040 -> b6502040
Password
  Default: icd2012

## Slide 11: Change your password

## Slide 12: Change the environment file name
Change the name of .cshrc
  mv .cshrc .cshrc_new
  Otherwise, you can not connect to workstation by SFTP

## Slide 13: SSH File Transfer Protocol (SFTP)
SFTP software
  SSH2 in Cuteftp
  SSH in FileZilla
Ex: FileZilla

## Slide 14: SSH in FileZilla (1/2)

## Slide 15: SSH in FileZilla (2/2)

## Slide 16: Simple Linux command
Source the setting file
  source
Change your password
  passwd
Document management
  cd [directory name/..]
  ls [-a/-l]
  mkdir [directory name]
  cp [options] [source] [destination]
  rm [-fir] [file/directory]
  mv [-fiu] [source] [destination]
  whereis/locate/find [file name]
Text Editor
  vi or vim
View Ref[2] for more detail!

## Slide 17: Vim

## Slide 18: Vim (insert mode)
Press “I”

## Slide 19: Vim
Enter “:wq”

## Slide 20: Flow chart
Cadence
Calibre
Nanosim
Your job
(Write netlist)
Layout
netlist
Post-layout simulation
*.fsdb
Extraction
Your job
(Give input)
nWave
.netlist .pex .pxi nn018.l

## Slide 21: Cadence Tools
  SPICE language (Assemble transistors)
  Layout parameter extraction

## Slide 22: Source the needed files
Source your environment setting file
  source .cshrc_new
Cadence tool
  source /usr/cadence/cshrc
Calibre tool
  source /usr/mentor/CIC/calibre.cshrc

## Slide 23: To run Cadence…
Make new dictionary
  mkdir hw2
  cd hw2
  mkdir calibre
  cd calibre
Copy necessary file
  cp /home/raid2_2/course/icd/cds.lib .
  cp /home/raid2_2/course/icd/display.drf .
  cp /home/raid2_2/course/icd/.cdsinit .
  cp /home/raid2_2/course/icd/lpe.cmd .
Run cadence
  icfb &
Your home directory
hw2
calibre
…
…
Remember to create an individual directory “calibre”
because Calibre will produce many temporary files.

## Slide 24: Open a layout (1/2)
File  open

## Slide 25: Open a layout (2/2)

## Slide 26: Write your netlist file from the layout view
**********************************************
* Main Circuit Netlist:
**********************************************
.subckt ND3 Z A B C
MN0 Z C n01 gnd n w=0.45u l=0.18u
MN2 n12 A gnd gnd n w=0.45u l=0.18u
MN1 n01 B n12 gnd n w=0.45u l=0.18u
MP0 Z A vdd vdd p w=0.9u l=0.18u
MP1 Z B vdd vdd p w=0.9u l=0.18u
MP2 Z C vdd vdd p w=0.9u l=0.18u
.ends ND3
S
G
D
B
G
D
S
B

## Slide 27: Run Calibre-PEX

## Slide 28: Initialization
Choose Cancel for your first time.
Choose OK if you have saved your setting before.

## Slide 29: PEX Rule setting
Run the rule file in the TA’s directory!
Specify your run directory

## Slide 30: Read Layout view and Netlist file
Make sure your layout view is open!
Specify your netlist file.

## Slide 31: Specify the Output Requirement
The name of your output netlist.

## Slide 32: Check run control settings and Run!

## Slide 33: After PEX finishes, check error!

## Slide 34: Three output files
Output files:
  *.pex.netlist
  *.pex.netlist.pex
  *.pex.netlist.*.pxi

## Slide 35: Post-layout Simulation Tools
  Nanosim
  SPICE language (Input waveform)

## Slide 36: Prepare for simulation
Revise *.pex.netlist (Attention!!)
  N  nch
  P  pch
Give input voltage source
  Piecewise linear voltage source VA connected between node 1 and node 2
    VA node1 node2 PWL 0n 0v 30n 0v
    + 30.5n 1.8v 60n 1.8v 60.5n 0v 70n 0v
  DC voltage source
    VA node1 node2 dc 1.8v
  Check Ref[1] for detail
node1
node2

## Slide 37: Revision example
Library from TA’s directory
Add your input source
N  nch
P  pch
Add setting

## Slide 38: Nanosim: Source file and execute
Source file
  source /usr/cad/synopsys/CIC/nanosim.cshrc
Execute
  nanosimgui &

## Slide 39: Create a new simulation work
Simulation  new
Give your simulation file name.

## Slide 40: Input *.netlist file
Select your revised netlist from cadence tool.

## Slide 41: Simulation setup

## Slide 42: Compile your netlist
Compile message

## Slide 43: Select the nodes to be observed

## Slide 44: Ready to run simulation

## Slide 45: Start simulation
If there is no error, your can check your signal data: *.fsdb file

## Slide 46: Debug Tool
  nWave

## Slide 47: nWave: Source file and execute
Source
  source /usr/spring_soft/CIC/verdi.cshrc
Execute nWave
  nWave &

## Slide 48: Select output file generated by Nanosim
You can use filter here to get your signal file.

## Slide 49: Select desired signals
Select the desired signal.

## Slide 50: Check your output waveform !

## Slide 51: Flow chart
Cadence
Calibre
Nanosim
Your job
(Write netlist)
Layout
netlist
Post-layout simulation
*.fsdb
Extraction
Your job
(Give input)
nWave
.netlist .pex .pxi nn018.l
Ex: ND3netlist
Ex:
ND3.pex.netlist
ND3.pex.netlist.pex
ND3.pex.netlist.ND3.pxi
Ex: ND3_HW2.fsdb

## Slide 52: Reminder
Be patient and careful about each step!
References
  [1] “SPICE,” CIC handout, 2001
  [2] “鳥哥的Linux 私房菜” http://linux.vbird.org/
If you have any questions, please contact…
  b96901055@ntu.edu.tw
  r00943118@ntu.edu.tw
    Specify [IC_Design] before your title
  課程網頁討論看板

## Slide 53: Thanks for your attention!
Q & A