## Slide 1: IC Design HW3 Tutorial
Chun-Yuan Chu
Advisor：Tzi-Dar Chiueh
2012/11/20

## Slide 2: Outline
Introduction to Verilog
  Module
  Value & number
  Data type
Verilog-XL simulation & nWave tool

## Slide 3: Introduction to Verilog
Module
Value & Number
Data Type

## Slide 4: What is Verilog
Verilog is a Hardware Description Language (HDL)
  Describe digital electronic system at multiple levels of abstraction
  Model the timing
  Express the concurrency of the system operation
  Test the system

## Slide 5: Verilog-Supported Levels of Abstraction
Behavioral level
  Describe a system by the flow of data between its functional blocks. It is used when we don't worry about how the hardware looks-like. We use this to model any block if we just know how the input output should be.
Register Transfer Level (RTL)
  Describe a system by the flow of data and control signals between and within its functional blocks
Gate level
  Describe a system by connecting predefined components

## Slide 6: The Verilog Module
Basic building blocks .
Begin with module,
end with endmodule
module <module name>(<port lists>);
//module description
endmodule

## Slide 7: Module Ports
Modules communicate through ports
  input
  output
  inout (bidirectional)
module FD2 (Q, D, CLK, RESET);
output Q; input CLK, D, RESET;
//module description
endmodule
FD2
D
CLK
RESET
Q

## Slide 8: 4-Value Logic System
0
  zero, false, low
1
  one, true, high
Z
  high impedance, floating
X
  unknown, occurs at un-initialized storage elements or un-resolvable logic conflicts

## Slide 9: Value and Number
[[<size>]’<radix>]<value>
  Size
    The size in bits
    Default size is 32 bits
  Radix
    b (binary), o (octal), d (decimal), h (hexadecimal)
    Default radix is decimal
  Value
    Any legal number in selected radix, including “x” and “z”
Radix and value are case-insensitive

## Slide 10: Value and Number – Examples
659 //unsized decimal
’h87ff //unsized hexadecimal
4af // illegal syntax
4’b1001 // 4-bit binary
5’d3 // 5-bit decimal
3’b01x // 3-bit binary with unknown LSB
12’hx // 12-bit unknown
8’d -6 // illegal syntax
-8’d 6 // phrase as -(8’d6)
underline usage
  27_195_000
  16’b0001_0101_0001_1111
  32’h12ab_f001
X and Z is sign-extended
  Ex. 12-bit a
    a = ’h x; // yields xxx
    a = ’h 3x; // yields 03x
    a = ’h 0x; // yields 00x

## Slide 11: Data Type Classes
wire
  wire [MSB:LSB] variables;
  input, inout, output are default to be wire.
  Used to describe combinational circuit!
reg
  reg [MSB:LSB] variables;
  Used to describe combinational or sequential circuit.

## Slide 12: Assign a value to wire
wire
  “assign “
    wire a;
    assign a = 1’b1;
  Output port
    wire a;
    wire b;
    assign b = 1’b0;
    NOT n0(a, b);
Every wire can be only assigned once!!!
    wire a;
    wire b;
    assign b = 1’b0;
    NOT n0(a, b);
    assign a = 1’b0; //Wrong!!!

## Slide 13: Module Instances (1/2)
Create a higher-level system by connecting lower-level components
module Reg2 (q, d, clk, rst);
output [1:0] q; input [1:0] d; input clk, rst;
FD2 f0(q[0], d[0], clk, rst); FD2 f1(.Q(q[1]), .D(d[1]), .CLK(clk), .RESET(rst));
endmodule
FD2
d[0]
clk
rst
q[0]
FD2
d[1]
q[1]
Reg2

## Slide 14: Module Instances (2/2)
module Reg2_2 (q, d, clk, rst);
output [1:0] q; input [1:0] d; input clk, rst;
wire [1:0] w;
Reg2 r0(w, d, clk, rst); Reg2 r1(q, w, clk, rst);
endmodule
q
Reg2
d
clk
rst
Reg2
2
2
2
Reg2_2
w

## Slide 15: Net Concatenations
Representation | Meaning
{b[3:0],c[2:0]} | {b[3] ,b[2] ,b[1] ,b[0], c[2] ,c[1] ,c[0]}
{a,b[3:0],w,3’b101} | {a,b[3] ,b[2] ,b[1] ,b[0],w,1’b1,1’b0,1’b1}
{4{w}} | {w,w,w,w}
{b,{3{a,b}}} | {b,a,b,a,b,a,b}

## Slide 16: Standard Cell Library (lib.v)
Choose what you need
Compose your circuit according to I/O connections
module AN3(Z,A,B,C);
output Z;
input A,B,C;
// netlist
and g1(Z,A,B,C);
// specify block, declare local
// timing constant
specify
// delay parameters
specparam Tp_A_Z = 0.275;
specparam Tp_B_Z = 0.275;
specparam Tp_C_Z = 0.275;
// path delay (full connection)
( A *> Z ) = ( Tp_A_Z );
( B *> Z ) = ( Tp_B_Z );
( C *> Z ) = ( Tp_C_Z );
endspecify
endmodule

## Slide 17: Standard Cell Library (lib.v)
AN3
AN4
AN2
EN //xnor
EN3
EO // xor
EO3
FA1 // full adder
FD1 // DFF
FD2
HA1 // half adder
IV // not
MUX21H
// 2-to-1 MUX
ND2 // nand
ND3
ND4
NR2 //nor
NR3
OR2
OR3
OR4

## Slide 18: Notification
In this HW, all the logic operation MUST consist of standard cell. You can NOT use logic operators.
  wire a, b, c;
  assign a = b & c;
  wire a, b, c;
  AN2 an(a, b, c);

## Slide 19: Example
module ADDER (out, in1, in2);
output [2:0] out;
input [1:0] in1, in2;
wire c;
FA1 fa0(c, out[0], in1[0], in2[0], 1’b0);
FA1 fa1(out[2], out[1], in1[1], in2[1], c);
endmodule

## Slide 20: Flow chart
Verilog
Your job
(Write Verilog file)
tb_Comparator_51.v
lib.v
answer.dat
in0.dat
in1.dat
in2.dat
in3.dat
in4.dat
Comparator_51.v
*.fsdb
nWave
All these files should be placed under the same folder

## Slide 21: Your Job
module COMPARATOR_51(median, i0, i1, i2, i3, i4);
output [2:0] min; input [5:0] i0, i1,i2, i3, i4;
\\ Write your design here
wire [?:0] …;
My_module_0 M0(?, ?, … , ?);
…….. My_module_x Mx(?, ?, … , ?);
endmodule
min
My_module_0
i0
6
3
COMPARATOR_51
i1
6
i2
6
i3
6
i4
6
My_module_x
?

## Slide 22: Verilog-XL Simulation & nWave Tool

## Slide 23: Test and verification your circuit
By applying input patterns and observing output responses
Test patterns
Device under test (*.v)
Output response
Testbench
(tb_*.v)
(*.fsdb)
Device under test (*.v)
(tb_*.v)
(*.fsdb)

## Slide 24: Compile and debug (1/2)
Source
  source .cshrc_new
  source /usr/cadence/cshrc
  source /usr/spring_soft/CIC/verdi.cshrc
Include the testbench & lib.v files to run simulation
  ncverilog +access+r tb_Comparator_51.v lib.v Comparator_51.v

## Slide 25: Compile and debug (2/2)

## Slide 26: Execute nWave & Open *.fsdb
Execute : nWave &
Open waveform file:
  File -> Open -> Comparator_51.fsdb

## Slide 27: Get signals

## Slide 28: Find Top Module & Choose signals

## Slide 29: Change the radix to be decimal

## Slide 30: Reminder
Due to 12/4 9:10AM in class!!
Please use cad 32~33 (for ncverilog & nWave)
Any further questions
  b96901055@ntu.edu.tw
  r00943118@ntu.edu.tw
To know more about Verilog, refer to
  http://www.ece.umd.edu/courses/enee359a.S2008/verilog_tutorial.pdf